## Slide 1
Each gate has the following:
Lights showing the state of all Inputs and Outputs
A 3D printed case that resembles the symbol used in circuits
Pins for Inputs and Sockets for Outputs
2 Buttons that supply power to the PCB
_____
Q = (A+B)
Department of Electrical and Computer Engineering
Iowa State Honors Poster Presentation
May 1st 2024
Jonathan Hess
Digital Logic Lab Tool: Hands on Learning
Rev 1 Gate PCB
Half Adder Circuit
https://github.com/Jetsama/DigitalLogicProject
Background:
Digital logic is the basis for all computer and digital systems
Digital logic and the math that surrounds it could be understood by students in middle/high school
Digital logic builds upon itself to create complexity by combing simple gates in more interesting ways
Previous physical examples require power and wire management
A | B | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
C = A * B
S = A⊕B
Goals for Project
Use only open-source tools such as KiCad to allow teachers/students to edit the design in the future.
Reduce costs to maximize the number of gates per kit.
Make source code, PCBs, and BOM available for anyone to create, edit, or manufacture themselves.
Create a booklet that teaches using puzzles and fun challenges.
Design:
The logic gate’s design needed to be small enough to allow for complex circuits but big enough to be handled easily.
There is 10 logic gates of each type to allow for building of larger circuits.
The board is expandable both to save on cost and for scalability.
One PCB is used for all the basic logic gates by swapping the logic IC.
Advised by Alexander Stoytchev
Introduction:
The project takes the abstract logic gates from computer engineering and creates physical representations that can be played and experimented with. This can make the learning of digital logic more fun and intuitive! Because of the nature of digital logic, students of all different knowledge levels can use these basic gates to create more interesting circuits.
Final Logic Gates Design:
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Q = A * B
AND
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Q = A + B
OR
A | Q
0 | 1
1 | 0
Q = Ā
NOT
S | Q
0 | A
1 | B
_
Q = S*A + S*B
MULTIPLEXER
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Q = A ⊕ B
XOR
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
_____
Q = (A*B)
NAND
A | B | Q
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR
Original PCB Design
Rev 2 Gate PCB
Rev 1 Mux PCB
Rev 1 Board PCB
Scalability via Multiple Board PCB Layout
Board with XOR and AND Gates
Rev 1 Inputs PCB
Rev 1 Outputs PCB
Special thanks to the ETG for all the help and consultation!
AND
XOR